## Slide 1
ELECTRIC POWER TRANSMISSION ENHANCEMENT
A Case of Nigerian Electric Power Grid

## Slide 2
  Introduction
  Transmission Line Performance
  Nigerian 330kv Power Grid; A Test Case
  Observation and Discussion
  Conclusion
  References
CONTENT

## Slide 3
INTRODUCTION
  Increase in Demand
    Economic activities and population growth have led to an increase in electrical energy demands
  Overutilization of Energy
    Overutilization of the transmission system has resulted in power quality reduction and limitations in power transmission.

## Slide 4
  Modeling Transmission Lines
  Enhancing Transmission Capabilities
  Analyzing Model Strengths and Weaknesses
  Assessing Enhancement Impacts
  Improving Asset Management
OBJECTIVES

## Slide 5
  Installation of New Transmission Line.
  Reconductoring Transmission Line/Terminal Equipment Replacements.
  Conversion from single circuit to double circuit.
  Voltage Upgrade.
  Reactive Power Compensation.
  Phase Shifting.
TRANSMISSION SYSTEMS ENHANCEMENT STRATEGIES

## Slide 6
  The Nigerian 330kV power grid faces problems like poor voltage, insufficient power, and frequent breakdowns.
  It cannot transmit the current power demand and would struggle even more with increased demand.
  Evaluating specific transmission lines is essential to improve performance and meet growing electricity needs.
  "Voltage upgrade" strategy implemented in Nigeria's transmission system.
NIGERIAN TEST CASE ON 330KV

## Slide 7
  Effect of Increase in Voltage Level
    Higher voltage boosts line loadability, asset utilization, and stability limits.
  Open-Line Characteristics
    No-load voltage may surpass limits for longer lines, requiring shunt reactors for regulation.
  Line’s Voltage Profile
    Increasing sending power decreased receiving voltage, causing violation, highlighting line capacity limits and inefficiencies.
  Effect of Line Reconductoring
    Reconductoring transmission line increases thermal capacity, not affecting voltage stability.
OBSERVATION

## Slide 8
  The lines in the 330KV transmission network are not limited by stability limits and thermal limits.
  Reconductoring, as a power grid strengthening strategy, may not yield a reasonable improvement on the grid
  Though transmission at Ultra High Voltage (UHV) levels can create rooms for more power evacuation.
  The power grid should be fortified with voltage control equipment
CONCLUSION

## Slide 9
  E. U. Oleka, S. N. Ndubisi, and G. K. Ijemaru, “Electric Power Transmission Enhancement: A case of nigerian electric power grid,” American Journal of Electrical and Electronic Engineering, http://pubs.sciepub.com/ajeee/4/1/5/ (accessed Apr. 5, 2024).
REFERENCES

## Slide 10
THANK YOU
PRESENTED BY
KAILASH DUSAD -- 22110112
MONU SUNIA -- 22110155
CHANCHAL YADAV -- 22110055